A Tutorial on
Acoustical Transducers:
Microphones and Loudspeak
A Tutorial on
Acoustical Transducers:
Microphones and Loudspeakers
Robert C. Maher
Montana State University
EELE 417/517 Acoustics and Audio Engineering
Fall 2016

---
Outline
Outline
- Introduction: What is sound?
- Microphones
  - Principles
  - General types
  - Sensitivity versus Frequency and Direction
- Loudspeakers
  - Principles
  - Enclosures
- Conclusion

---
Transduction
Transduction
- Transduction means converting energy from one form to another
- Acoustic transduction generally means converting sound energy into an electrical signal, or an electrical signal into sound
- Microphones and loudspeakers are acoustic transducers

---
Acoustics and Psychoacoustics
Mechanical
to
Acoustical
Electrical
to
Psychological
Acoustical propagation (reflection, diffraction, absorption, etc.)
Mechanical to
Electrical (nerve signals)
Acoustical
to
Mechanical

---
What is Sound?
What is Sound?
- Vibration of air particles
- A rapid fluctuation in air pressure above and below the normal atmospheric pressure
- A wave phenomenon: we can observe the fluctuation as a function of time and as a function of spatial position

---
Sound (cont.)
Sound (cont.)
- Sound waves propagate through the air at approximately 343 meters per second
  - Or 1125 feet per second
  - Or 4.7 seconds per mile ≈ 5 seconds per mile
  - Or 13.5 inches per millisecond ≈ 1 foot per ms
- The speed of sound (c) varies as the square root of absolute temperature
  - Slower when cold, faster when hot
  - Ex: 331 m/s at 32ºF, 353 m/s at 100ºF

---
Sound (cont.) (2)
Sound (cont.)
- Sound waves have alternating high and low pressure phases
- Pure tones (sine waves) go from maximum pressure to minimum pressure and back to maximum pressure. This is one cycle or one waveform period (T).
T

---
Wavelength and Frequency
Wavelength and Frequency
- If we know the waveform period and the speed of sound, we can compute how far the sound wave travels during one cycle. This is the wavelength (λ).
- Another way to describe a pure tone is its frequency (f): how many cycles occur in one second.

---
Capturing Sound Waves
Capturing Sound Waves

---
Wave Relationships
Wave Relationships
- c = f · λ [m/s = /s · m]
- T = 1/f
- λ = T · c
  - c = speed of sound [m/s]
  - f = frequency [ /s]
  - λ = wavelength [ m ]
  - T = period [ s ]
  - Note: high frequency implies short wavelength, low frequency implies long wavelength

---
Sound Amplitude and Intensity
Sound Amplitude and Intensity
- The amount of pressure change due to the sound wave is the sound amplitude
- The motion of the air particles due to the sound wave can transfer energy
- The rate at which energy is delivered by the wave is the sound power [ W (watts)]
- The power delivered per unit area is the sound intensity [ W/m2 ]

---
Microphone Principles
Microphone Principles
- Concepts:
  - Since sound is a pressure disturbance, we need a pressure gauge of some sort
  - Since sound exerts a pressure, we can use it to drive an electrical generator
  - Since sound is a wave, we can measure simultaneously at two (or more) different positions to figure out the direction the wave is going

---
Microphone:  Diaphragm and Generating Element
Microphone: Diaphragm and Generating Element
- Diaphragm: a membrane that can be set into motion by sound waves
  - Sensitivity: how much motion from a given sound intensity
- Generating Element: an electromechanical device that converts motion of the diaphragm into an electrical current and voltage
  - Sensitivity: how much electrical signal power is obtained from a given sound intensity

---
Electrical Generators
Electrical Generators
- Variable Resistor
- Variable Inductor
- Electromagnetic
- Variable Capacitor
- Piezoelectric
- Other exotic methods…

---
The First Microphones…
The First Microphones…
Alexander Graham Bell (variable resistor)
Carbon granules (variable resistor)
Battery
+
-
Acid water
Battery
+
-

---
Ribbon Microphone
Ribbon Microphone
Diaphragm
(metallic foil)
N
S
Electrical Circuit
Magnet

---
Dynamic Microphone
Dynamic Microphone
Diaphragm moves a coil of wire through a fixed magnetic field: Faraday’s Law indicates that a voltage is produced
N
S

---
Piezoelectric Microphone
Piezoelectric Microphone
- Piezoelectric generating element: certain crystals produce a voltage when distorted (piezo means “squeeze” in Greek)
- Diaphragm attached to piezo element
- Rugged, reasonably sensitive, not particularly linear

---
Capacitor (Condenser) Mic
Capacitor (Condenser) Mic
- Variable electrical capacitance
  - British use the word “condenser”
- Currently the best for ultra sensitivity, low noise, and low distortion (precision sound level meters use condenser mics
- Difficult to manufacture, delicate, and can be too sensitive for some applications

---
Condenser Mic (cont.)
Condenser Mic (cont.)
- Capacitance = charge / voltage
- Capacitance ≈ ε A / d
A = area, d=distance between plates
ε = permittivity
signal voltage ≈ d · (charge / (ε · A))
Diaphragm
Backplate
High impedance preamp
constant

---
Microphone Patterns
Microphone Patterns
- A single diaphragm acts like a pressure detector
- Two diaphragms can give a directional preference
- Placing the diaphragm in a tube or cavity can also give a directional preference

---
Microphone Patterns (cont.)
Microphone Patterns (cont.)
- Omnidirectional: all directions
- Unidirectional or Cardioid: one direction
- Bi-directional or ‘figure 8’: front and back pickup, side rejection

---
Microphone Coloration
Microphone Coloration
- Most microphones are not equally sensitive at all frequencies
  - The human ear is not equally sensitive at all frequencies either!
- The frequency (and directional) irregularity of a microphone is called coloration
- Example: Stereophile Microphone .wav

---
Producing Sound Waves

---
Loudspeakers
Loudspeakers

---
Loudspeakers (2)
Loudspeakers
- Diaphragm attached to a motor element
- Diaphragm motion is proportional to the electrical signal (audio signal)
- Efficiency: how much acoustical power is produced from a given amount of input electrical power

---
Moving Coil Driver
Moving Coil Driver
Current through coil creates a magnetic force relative to the fixed magnet
Cone
Magnet
Voice Coil
Speaker Frame

---
Mechanical Challenges
Mechanical Challenges
- Large diameter diaphragm can produce more acoustic power, but has large mass and directional effects
- Diaphragm displacement (in and out) controls sound intensity, but large displacement causes distortion
- Result: low frequencies require large diameter and large displacement

---
Unbaffled Driver
Unbaffled Driver
Air has time to “slosh” between front and back at low frequencies: poor bass response

---
Baffled Driver (flush mount)
Baffled Driver (flush mount)
Baffle prevents front-back interaction: improved low frequency performance

---
Loudspeaker Enclosure
Loudspeaker Enclosure
- Enclosure is a key part of the acoustical system design
- Sealed box or acoustic suspension
  - enclosed air acts like a spring
- Vented box or bass-reflex
  - enclosed air acts like a resonator
- Horns and baffles

---
Acoustic Suspension
Acoustic Suspension
Sealed box acts as a stiff “air spring”
Enclosed volume chosen for optimum restoring force
Relatively weak (compliant) cone suspension
Greatly reduced nonlinear distortion!

---
Ported (Resonant) Enclosure
Ported (Resonant) Enclosure
Ported box is a Helmholtz resonator.
Enclosed volume and port size chosen to boost acoustic efficiency at low frequencies: reduces required cone motion for a given output, allowing lower distortion.
Driver acts as a direct radiator at frequencies above box resonance.
Port (hole): radiates only at frequencies near box resonant frequency, but reduces cone motion.

---
Other Loudspeaker Issues
Other Loudspeaker Issues
- Multi-way loudspeakers: separate driver elements optimized for low, mid, and high frequencies (woofer, squawker, tweeter)
- Horns: improve acoustical coupling between driver and the air
- Transmission line enclosures
- Electrostatic driver elements
- ‘Powered’ speakers

---
Conclusions
Conclusions
- Microphone: a means to sense the motion of air particles and create a proportional electrical signal
- Loudspeaker: a means to convert an electrical signal into proportional motion of air particles
- Engineering tradeoffs exist: there is not a single best solution for all situations

---
Speakers: Inverse Eardrums
Speakers: Inverse Eardrums
- Speakers vibrate and push on the air
  - pushing out creates compression
  - pulling back creates rarefaction
- Speaker must execute complex motion according to desired waveform
- Speaker is driven via “solenoid” idea:
  - electrical signal (AC) is sent into coil that surrounds a permanent magnet attached to speaker cone
  - depending on direction of current, the induced magnetic field either lines up with magnet or is opposite
  - results in pushing or pulling (attracting/repelling) magnet in coil, and thus pushing/pulling on center of cone

---
Speaker Geometry
Speaker Geometry

---
Push Me, Pull Me
Push Me, Pull Me
- When the center of the speaker cone is kicked, the whole cone can’t respond instantaneously
  - the fastest any mechanical signal can travel through a material is at the speed of sound in the material
- The whole cone must move into place well before the wave period is complete
  - otherwise, different parts of the cone might be moving in while others are moving out (thus canceling the sound)
  - if we require the signal to travel from the center to the edge of the cone in 1/N of a wave cycle (N is some large-ish number):
    - available time is t = 1/Nf = /Ncair
    - ripple in cone travels cconet, so radius of cone must be < ccone/Ncair
  - basic point is that speaker size is related to wavelength of sound
    - low frequency speakers are big, high frequency small

---
The Look of Sound
The Look of Sound
Sound Waveforms
Frequency Content
Digital Sampling

---
All Shapes of Waveforms
All Shapes of Waveforms
- Different Instruments have different waveforms
  - a: glockenspiel
  - b: soft piano
  - c: loud piano
  - d: trumpet
- Our ears are sensitive to the detailed shape of waveforms!
- More waveforms:
  - e: french horn
  - f: clarinet
  - g: violin
http://www.st-and.demon.co.uk/AudioMisc/asymmetry/asym.html

---
How does our ear know?
How does our ear know?
- Our ears pick out frequency components of a waveform
- A DC (constant) signal has no wiggles, thus is at zero frequency
- A sinusoidal wave has a single frequency associated with it
- The faster the wiggles, the higher the frequency
- The height of the spike indicates how strong (amplitude) that frequency component is

---
Composite Waveforms
Composite Waveforms
- A single sine wave has only one frequency represented in the “power spectrum”
- Adding a “second harmonic” at twice the frequency makes a more complex waveform
- Throwing in the fourth harmonic, the waveform is even more sophisticated
- A square wave is composed of odd multiples of the fundamental frequency

---
Decomposing a Square Wave
Decomposing a Square Wave
- Adding the sequence:
  - sin(x) + 1/3sin(3x) + 1/5sin(5x) + 1/7sin(7x) + …
  - leads to a square wave
  - Fourier components are at odd frequency multiples with decreasing amplitude

---
The ear assesses frequency content
The ear assesses frequency content
- Different waveforms look different in frequency space
- The sounds with more high-frequency content will sound raspier
- The exact mixture of frequency content is how we distinguish voices from one another
  - effectively, everyone has their own waveform
  - and corresponding spectrum
  - though an “A” may sound vastly similar, we’re sensitive to very subtle variations

---
Assignments
Assignments
- Read pp. 404–406, 489–492
- Midterm 05/04 (Thu.) 2PM WLH 2005
  - have posted study guide on course website
  - will have review session Wednesday 7:00–8:50, Center 113
  - Use light-green Scantron: Form No.: X-101864
  - Bring #2 pencil, calculators okay