Datu aizsardzība un drošība
2. lekcija
Valdis Vītoliņš

---
Kriptogrāfija u.c. vārdi
- Kriptogrāfija (no lat. kryptós) ir praktiska zinātne kurā pēta, kā padarīt drošu saziņu, datu veselumu (integrity), patiesumu (authenticy) un pretnoliegšanu (non-repudiation)
- Augšminēto parasti nodrošina šifrējot datus vai datu straumi
- Kriptoloģija ir zinātne par šifrēšanas paņēmieniem un to "stipruma" novērtēšanu
- Kriptoanalīze ir zinātne par šifru īpašībām un to uzlaušanas veidiem ātrāk kā ar pilno pārlasi

---
Kerckhoff’s principle
Svarīgi principi
Kerkofa (Auguste Kerckhoffs) princips
"Šifrēšanas algoritmam ir jābūt drošam arī tad, ja viss, izņemot šifrēšanas atslēgu, ir labi zināms."
Brūsa Šneijera (Bruce Schneier) princips
"Jebkurš var izdomāt tik gudru šifrēšanas algoritmu, ka viņš pats to nespēj uzlauzt."

---
Cryptographic Tools
Šifrēšanas veidi
- Galvenie šifrēšanas veidi ir:
  - Simetriskā šifrēšana
    - Pārstatīšanas (transposition)
    - Aizstāšanas (substitution)
    - Abu augšminēto apvienojums
  - Asimetriskā šifrēšana
    - Izmanto publisko-privāto atslēgu pārus
- Pēc datu veida izšķir
  - Bloku šifrēšanu — šifrē noteikta izmēra blokus
  - Straumes šifrēšanu — šifrē patvaļīga garuma bitu straumes
[Speaker Notes: An important element in many computer security services and applications is the use of cryptographic algorithms. This chapter provides an overview of the various types of algorithms, together with a discussion of their applicability. For each type of algorithm, we introduce the most important standardized algorithms in common use. We begin with symmetric encryption, which is used in the widest variety of contexts,primarily to provide confidentiality. Next, we examine secure hash functions and discuss their use in message authentication. The next section examines public-key encryption, also known as asymmetric encryption. We then look in at the two most important applications of public-key encryption, namely digital signatures and key management. In the case of digital signatures, asymmetric encryption and secure hash functions are combined to produce an extremely useful tool. Finally, in this chapter we provide an example of an application area for cryptographic algorithms by looking at the encryption of stored data.]

---
Symmetric Encryption
Simetriskā šifrēšana
[Speaker Notes: The universal technique for providing confidentiality for transmitted data is symmetric encryption. Symmetric encryption, also referred to as conventional encryption or single-key encryption, was the only type of encryption in use prior to the introduction of public-key encryption in the late 1970s. Countless individuals and groups, from Julius Caesar to the German U-boat force to present-day diplomatic, military, and commercial users, use symmetric encryption for secret communication. It remains by far the more widely used of the two types of encryption. A symmetric encryption scheme has five ingredients, as shown here in Figure 2.1 from the text. • Plaintext: This is the original message or data that is fed into the algorithm as input. • Encryption algorithm: The encryption algorithm performs various substitutions and transformations on the plaintext. • Secret key: The secret key is also input to the encryption algorithm. The exact substitutions and transformations performed by the algorithm depend on the key. • Ciphertext: This is the scrambled message produced as output. It depends on the plaintext and the secret key. For a given message, two different keys will produce two different ciphertexts. • Decryption algorithm: This is essentially the encryption algorithm run in reverse. It takes the ciphertext and the secret key and produces the original plaintext. There are two requirements for secure use of symmetric encryption: 1. We need a strong encryption algorithm. 2. Sender and receiver must have secure obtained, & keep secure, the secret key.]

---
Klasiski simetriskie šifri
- Pārstatīšanas šifri
  - Redeļu žogs (rail fence) — šifrējot burus raksta izlaižot noteiktu vietu skaitu, un, kad nonāk līdz beigām, aizpilda nākamo brīvo vietu
  - Kolonnu un rindu pārstatīšana
  - Maskas (grila) šifrs — tekstu ieraksta noteiktā maskā, pārējo aizpilda ar troksni
- Aizstāšanas šifri
  - Cēzara šifrs nobīda burtu par noteiktu vietu skaitu
  - ROT13 simetrisks latīņu burtu šifrs
  - Vižnē (Vigenère) — nobīda burtus atkarībā no izvēlētās atslēgas
  - Vienreiz lietojama atslēga (One-time pad)

---
Attacking Symmetric Encryption
Simetrisko šifru uzlaušana
- Kriptoanalīze izmanto
  - Šifrēšanas algoritmu īpašības
  - Nešifrētā teksta īpašības
    - Burtu sadalījumu valodā
  - Zināmus šifrētu ziņojumu paraugus
    - Izplatītus vārdus un frāzes
- Pilnās pārlases paņēmiens
  - Ar "rupja spēka metodi" (brute-force method) veic pilnu šifrēšanas atslēgu/paņēmienu pārlasi, līdz atrod vajadzīgo
[Speaker Notes: There are two general approaches to attacking a symmetric encryption scheme. The first attack is known as cryptanalysis. Cryptanalytic attacks rely on the nature of the algorithm plus perhaps some knowledge of the general characteristics of the plaintext or even some sample plaintext-ciphertext pairs. This type of attack exploits the characteristics of the algorithm to attempt to deduce a specific plaintext or to deduce the key being used. If the attack succeeds in deducing the key, the effect is catastrophic: All future and past messages encrypted with that key are compromised. The second method, known as the brute-force attack, is to try every possible key on a piece of ciphertext until an intelligible translation into plaintext is obtained. On average, half of all possible keys must be tried to achieve success.]

---
Exhaustive Key Search
Pilnās pārlases paņēmiens
[Speaker Notes: Table 2.1 from the text shows how much time is involved for various key sizes. The table shows results for each key size, assuming that it takes 1 µs to perform a single decryption, a reasonable order of magnitude for today's computers. With the use of massively parallel organizations of microprocessors, it may be possible to achieve processing rates many orders of magnitude greater. The final column of the table considers the results for a system that can process 1 million keys per microsecond. At this performance level, a 56-bit key is no longer computationally secure. The assumption of one encryption per microsecond is overly conservative. The widely used encryption scheme, the Data Encryption Standard (DES) was finally and definitively proved insecure in July 1998, when the Electronic Frontier Foundation (EFF) announced that it had broken a DES encryption using a special-purpose "DES cracker" machine that was built for less than $250,000. The attack took less than three days. The EFF has published a detailed description of the machine, enabling others to build their own cracker [EFF98]. It is important to note that there is more to a key-search attack than simply running through all possible keys. Unless known plaintext is provided, the analyst must be able to recognize plaintext as plaintext. If the message is just plain text in English, then the result pops out easily. If the message is some more general type of data, such as a numerical file, and this has been compressed, the problem becomes even more difficult to automate. Thus, to supplement the brute-force approach, some degree of knowledge about the expected plaintext is needed, and some means of automatically distinguishing plaintext from garble is also needed. The EFF approach addresses this issue as well and introduces some automated techniques that would be effective in many contexts. Figure 2.2 shows how long it would take to crack a DES-style algorithm as a function of key size.]

---
Symmetric Encryption Algorithms
Modernie simetriskās šifrēšanas veidi
[Speaker Notes: The most commonly used symmetric encryption algorithms are block ciphers. A block cipher processes the plaintext input in fixed-size blocks and produces a block of ciphertext of equal size for each plaintext block. The algorithm processes longer plaintext amounts as a series of fixed-size blocks. The most important symmetric algorithms, all of which are block ciphers, are the Data Encryption Standard (DES), triple DES, and the Advanced Encryption Standard (AES); as summarized here in Table 2.2 from the text.]

---
DES and Triple-DES
DES un 3DES
- Data Encryption Standard (DES) bija plaši izmantots veids
  - izmanto 64 bitu atklāto tekstu un 56 bitu atslēgu, iegūstot 64 bitu šifrētu tekstu
  - Izmanto gan pārstatīšanu, gan aizstāšanu
    (Feistela šifru)
  - Darbības ir bitu orientētas
  - Principā ir drošs, bet mūsdienu datoriem 56 bitu atslēga ir par īsu
- Tāpēc izmanto 3DES (TDES, Tripple-DES)
  - Atkārto DES 3 reizes (2× nevar izmantot satikties-pa-vidu uzbrukuma dēļ)
  - Izmanto 2 vai 3 atslēgas
  - Drošāks, bet lēnāks par DES
[Speaker Notes: The most widely used encryption scheme is based on the Data Encryption Standard (DES) adopted in 1977 by the National Bureau of Standards, now the NIST, as FIPS PUB 46. The algorithm itself is referred to as the Data Encryption Algorithm (DEA). DES takes a plaintext block of 64 bits and a key of 56 bits, to produce a ciphertext block of 64 bits. Concerns about the strength of DES fall into two categories: concerns about the algorithm itself and concerns about the use of a 56-bit key. The first concern refers to the possibility that cryptanalysis is possible by exploiting the characteristics of the DES algorithm. Over the years, there have been numerous attempts to find and exploit weaknesses in the algorithm, making DES the most-studied encryption algorithm in existence. A more serious concern is key length. With a key length of 56 bits, there are 256 possible keys, which is approximately 7.2  1016 keys. As noted on the previous slide, this can now be broken relatively easily. The life of DES was extended by the use of triple DES (3DES), which involves repeating the basic DES algorithm three times, using either two or three unique keys, for a key size of 112 or 168 bits. Triple DES (3DES) was first standardized for use in financial applications in ANSI standard X9.17 in 1985. 3DES was incorporated as part of the Data Encryption Standard in 1999, with the publication of FIPS PUB 46-3. 3DES has two attractions that assure its widespread use over the next few years. First, with its 168-bit key length, it overcomes the vulnerability to brute-force attack of DEA. Second, the underlying encryption algorithm in 3DES is the same as in DEA. The principal drawback of 3DES is that the algorithm is relatively sluggish in software.]

---
Advanced Encryption Standard (AES)
AES
- AES — (Advanced Encryption Standard) pārstatīšana un aizstāšana ir baitu orientēta
- Izmanto galīgo lauku (Galuā, Gallois) aritmētiku
- Ieviesa kā DES pēcteci
  - 1997. g. NIST izsludināja konkursu 1997. g
  - 2001. g. izvēlējās Rijndael algoritmu
  - Publicēts kā FIPS 197 standarts
- Simetriska šifrēšana
- 128 bitu datu bloks, 128,192,256 bitu atslēgas
- Pamazām aizstāj 3DES
[Speaker Notes: Because of its drawbacks, 3DES is not a reasonable candidate for long-term use. As a replacement, NIST in 1997 issued a call for proposals for a new Advanced Encryption Standard (AES), which should have a security strength equal to or better than 3DES and significantly improved efficiency. In addition to these general requirements, NIST specified that AES must be a symmetric block cipher with a block length of 128 bits and support for key lengths of 128, 192, and 256 bits. Evaluation criteria included security, computational efficiency, memory requirements, hardware and software suitability, and flexibility. In 2001, AES was issued as a federal information processing standard (FIPS 197). In a first round of evaluation, 15 proposed algorithms were accepted. A second round narrowed the field to 5 algorithms. NIST completed its evaluation process and published a final standard (FIPS PUB 197) in November of 2001. NIST selected Rijndael as the proposed AES algorithm. AES is now widely available in commercial products.]

---
Block verses Stream Ciphers
Bloku un straumes šifri
- Bloku šifri ir piemēroti saglabātu datu šifrēšanai
- Datu pārraidei ir nepieciešami straumes šifri, ar kuriem var šifrēt patvaļīga garuma bitu straumes
- Parasti iegūst no bloku šifriem
[Speaker Notes: A block cipher processes the plaintext input in fixed-size blocks and produces a block of ciphertext of equal size for each plaintext block. The algorithm processes longer plaintext amounts as a series of fixed-size blocks. Typically, symmetric encryption is applied to a unit of data larger than a single 64-bit or 128-bit block. Plaintext sources must be broken up into a series of fixed-length block for encryption by a symmetric block cipher. The simplest approach to multiple-block encryption is known as electronic codebook (ECB) mode, in which plaintext is handled b bits at a time and each block of plaintext is encrypted using the same key. Typically b=64 or b=128. Figure 2.3a here shows the ECB mode. A plaintext of length nb is divided into n b-bit blocks. Each block is encrypted using the same algorithm and the same encryption key, to produce a sequence of n b-bit blocks of ciphertext. To increase the security of symmetric block encryption for large sequences of data, a number of alternative techniques have been developed, called modes of operation (see chapter 19). A stream cipher processes the input elements continuously, producing output one element at a time. Although block ciphers are far more common, there are certain applications in which a stream cipher is more appropriate. A typical stream cipher encrypts plaintext one byte at a time, as shown in Figure 2.3b. The output of a pseudorandom number generator (the keystream), is combined one byte at a time with the plaintext stream using the bitwise exclusive-OR (XOR) operation. With a properly designed pseudorandom number generator, a stream cipher can be as secure as block cipher of comparable key length.The primary advantage of a stream cipher is that stream ciphers are almost always faster and use far less code than do block ciphers.The advantage of a block cipher is that you can reuse keys.]

---
Straumes šifrēšana
- Electronic Codebook (ECB) izmanto to pašu atslēgu katram jaunam blokam
  - Tā pati atslēga tiek izmantota vairākkārt, ko var izmantot uzlaušanai
- Cipher Block Chaining (CBC) nākamā bloka atslēgai izmanto iepriekšējā bloka vērtību
  - Katram blokam ir sava šifrēšanas atslēga
- CBC ir dažādi varianti
  - Cipher Feedback (CFB) ir pašsinhronizējošs
  - Output Feedback (OFB) pieļauj kļūdu korekciju
  - Counter (CTR) var darbināt paralēli

---
Message Authentication
Datu autentiskums
- Nodrošina aizsardzību pret datu bojājumiem
- Ļauj pārbaudīt, ka dati ir autentiski
  - Nav mainīts saturs
  - Nāk no patiesā piegādātāja
  - Ir pārraidīti pareizā secībā
- Var izmantot standarta šifrēšanu
  - Atslēga ir zināma tikai sūtītājam un saņēmējam
- Izmanto jaucējfunkciju
  - Jaucējvērtību pievieno ziņojumam ar zināmu algoritmu
[Speaker Notes: Encryption protects against passive attack (eavesdropping). Message authentication protects against active attacks (falsification of data and transactions), by verifying that received messages are authentic, that is that the contents of the message have not been altered and that the source is authentic. We may also wish to verify a message's timeliness and sequence relative to other messages flowing between two parties. It is possible to perform authentication simply by the use of conventional encryption. If we assume that only the sender and receiver share a key (which is as it should be), then only the genuine sender would be able to encrypt a message successfully for the other participant. Furthermore, if the message includes an error-detection code and a sequence number, the receiver is assured that no alterations have been made and that sequencing is proper. If the message also includes a timestamp, the receiver is assured that the message has not been delayed beyond that normally expected for network transit. Alternatively there are several approaches to message authentication that do not rely on encryption. In all of these approaches, an authentication tag is generated and appended to each message for transmission. The message itself is not encrypted and can be read at the destination independent of the authentication function at the destination.]

---
Secure Hash Functions
Jaucējfunkcijas darbības princips
[Speaker Notes: An alternative to the message authentication code is the one-way hash function. As with the message authentication code, a hash function accepts a variable-size message M as input and produces a fixed-size message digest H(M) as output (Figure 2.5). Unlike the MAC, a hash function does not also take a secret key as input. To authenticate a message, the message digest is sent with the message in such a way that the message digest is authentic.]

---
Hash Function Requirements
Jaucējfunkciju īpašības
- Ieejā var ievadīt patvaļīgu bitu daudzumu
- Izejā vienmēr ir nemainīgs bitu skaits
- Viegli rēķināt tiešā virzienā
  - Jaucējfunkciju H(x) dotam x ir viegli izrēķināt
- Grūti rēķināt pretēji
  - ir grūti izrēķināt noteiktu x, tā ka H(x) = h
- Laba sadursmju noturība
  - Ir grūti atrast y ≠ x tā, ka H(y) = H(x)
[Speaker Notes: The purpose of a hash function is to produce a "fingerprint" of a file, message, or other block of data. To be useful for message authentication, a hash function H must have the properties listed here. The first three properties are requirements for the practical application of a hash function to message authentication. The fourth property is the one-way property: it is easy to generate a code given a message, but virtually impossible to generate a message given a code. This property is important if the authentication technique involves the use of a secret value (such as shown in Figure 2.5c). The fifth property guarantees that it is impossible to find an alternative message with the same hash value as a given message. This prevents forgery when an encrypted hash code is used (as in Figures 2.5a and b). A hash function that satisfies the first five properties in the preceding list is referred to as a weak hash function. If the sixth property is also satisfied, then it is referred to as a strong hash function. The sixth property protects against a sophisticated class of attack known as the birthday attack. In addition to providing authentication, a message digest also provides data integrity. It performs the same function as a frame check sequence: if any bits in the message are accidentally altered in transit, the message digest will be in error.]

---
Varavīksnes tabulas
- Zināmām sākotnējām vērtībām var izveidot jaucējvērtību tabulu, piemēram:
  - MD5 30c6677b833454ad2df762d3c98d2409 ieejā ir apple
  - http://md5cracker.org/decrypted-md5-hash/30c6677b833454ad2df762d3c98d2409
- Izmantojot " t.s. "varavīksnes tabulas", var ātrāk atrast nelielas variācijas, piemēram, apple1
- Šādu uzlaušanu apgrūtina, pievienojot "sāli",
  piemēram, /etc/shadow fails:
  student:$6$F.uEoX7c$UCO85Yy/h5u4kjHUBxdZJ4jK29Rr.:16339:0:99999:7:::
  F.uEoX7c — sāls
  UCO85Yy/h5u4kjHUBxdZJ4jK29Rr. — paroles un sāls jaucējsumma

---
Hash Functions
Jaucējfunkcijas
- Divi uzlaušanas paņēmieni
  - Kriptoanalīze
    - Izmanto algoritmu ievainojamības
  - Pilnā pārlase
    - Mēģina visus variantus, kamēr atrod vajadzīgo
    - Vidējais meklējumu skaits atkarīgs no jaucējvērtības garuma 2n/2
- MD5
  - 128 bitu jaucējvērtība
- SHA
  - SHA1 — 160 bitu jaucējvērtība
  - SHA2 — 256, 384 vai 512 bitu jaucējvērtība
[Speaker Notes: As with symmetric encryption, there are two approaches to attacking a secure hash function: cryptanalysis and brute-force attack. As with symmetric encryption algorithms, cryptanalysis of a hash function involves exploiting logical weaknesses in the algorithm. The strength of a hash function against brute-force attacks depends solely on the length of the hash code produced by the algorithm. If strong collision resistance is required (and this is desirable for a general-purpose secure hash code), then the value 2n/2 determines the strength of the hash code against brute-force attacks. Oorschot and Wiener presented a design for a $10 million collision search machine for MD5, which has a 128-bit hash length, that could find a collision in 24 days. Thus a 128-bit code may be viewed as inadequate. With a hash length of 160 bits, the same search machine would require over four thousand years to find a collision. With today's technology, the time would be much shorter, so that 160 bits now appears suspect. In recent years, the most widely used hash function has been the Secure Hash Algorithm (SHA). SHA was developed by the National Institute of Standards and Technology (NIST) and published as a federal information processing standard (FIPS 180) in 1993. When weaknesses were discovered in SHA, a revised version was issued as FIPS 180-1 in 1995 and is generally referred to as SHA-1. SHA-1 produces a hash value of 160 bits. In 2002, NIST produced a revised version of the standard, FIPS 180-2, that defined three new versions of SHA, with hash value lengths of 256, 384, and 512 bits, known as SHA-256, SHA-384, and SHA-512. These new versions have the same underlying structure and use the same types of modular arithmetic and logical binary operations as SHA-1. In 2005, NIST announced the intention to phase out approval of SHA-1 and move to a reliance on the other SHA versions by 2010.]

---
Random Numbers
Gadījuma skaitļi
- Straumes šifros un nesimetriskā šifrēšanā ir svarīgi atrast gadījuma skaitļus
  - Tā, lai tie būtu vienmērīgi izkliedēti pieļautajās vērtībās
  - Tā, lai ar fiksētu algoritmu tie būtu varbūtīgi
- Praktiski vienmēr izmanto pseido-gadījumskaitļu ģeneratorus
[Speaker Notes: Random numbers play an important role in the use of encryption for various network security applications, such as in the generation of: keys for public-key algorithms, stream keys in a stream cipher, for temporary session keys, and in key distribution scenarios. These applications give rise to two distinct and not necessarily compatible requirements for a sequence of random numbers: randomness and unpredictability. Traditionally, the concern in the generation of a sequence of allegedly random numbers has been that the sequence of numbers be random in some well-defined statistical sense (such as uniform distribution and independence). In applications such as reciprocal authentication and session key generation, the requirement is not so much that the sequence of numbers be statistically random but that the successive members of the sequence are unpredictable. With “true” random sequences, each number is statistically independent of other numbers in the sequence and therefore unpredictable. However, as is discussed shortly, true random numbers are not always used; rather, sequences of numbers that appear to be random are generated by some algorithm. In this latter case,care must be taken that an opponent not be able to predict future elements of the sequence on the basis of earlier elements.]

---
Pseudorandom verses Random Numbers
Psedo- un īsti gadījumskaitļu ģeneratori
- Bieži izmanto, lai iegūtu gadījumsaitļiem līdzīgus skaitļus
  - Nodrošina skaitļu statistiskos parametrus
  - Var būt viegli aprēķināmi
- Īsti gadījumskaitļu ģeneratori izmanto patiesi varbūtīgus notikumus
  - Radiāciju, siltumu, strāvu
  - Mūsdienās bieži iekļauti dažādās aparatūrās
- Ir pseido-gadījumskaitļu ģeneratori, kas skaitļu secību aprēķina determinēti, bet kā "sēklu" izmanto troksni
  - Sistēmas atmiņu (entropiju), lietotāja ievadītos datu u.tml.
[Speaker Notes: Cryptographic applications typically make use of algorithmic techniques for random number generation. These algorithms are deterministic and therefore produce sequences of numbers that are not statistically random. However, if the algorithm is good, the resulting sequences will pass many reasonable tests of randomness. Such numbers are referred to as pseudorandom numbers. A true random number generator (TRNG) uses a nondeterministic source to produce randomness. Most operate by measuring unpredictable natural processes, such as pulse detectors of ionizing radiation events, gas discharge tubes, and leaky capacitors. Increasingly have true random sources in modern computer chips.]

---
Limitations of cryptography
Kriptogrāfijas trūkumi
Nedrošākā vieta parasti ir cilvēks
XKCD 538